## Slide 1
NUS
Mechanical Engineering
ME5400A PROJECT
Braitenberg-Based
Pursuit Behaviour
in Cluttered
Surveillance
Environments
Shridhar Iyer
A0329367R · Department of Mechanical Engineering
National University of Singapore

## Slide 2
INTRODUCTION
Motivation & Research Question
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
The Challenge
Autonomous surveillance robots must pursue intruders in real environments
Cluttered spaces (offices, warehouses) require reactive obstacle avoidance
Fixed-weight reactive controllers degrade severely with obstacle density
Deliberative planning introduces unacceptable latency for pursuit tasks
Research Question
How does obstacle density affect a Braitenberg pursuit controller, and can kinematic improvements + RL weight adaptation recover lost performance?
Three Objectives
i
Characterise
Quantify how obstacle density degrades pure reactive pursuit performance
ii
Identify
Diagnose the dominant failure modes: stalling vs. thrashing
iii
Evaluate
Test whether kinematic improvements + RL weight adaptation can recover performance

## Slide 3
SYSTEM ARCHITECTURE
Four-Stage Experimental Pipeline
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
1
Pure
Braitenberg
Original base,
fixed weights α, β
Tests:
Baseline
2
RL Adaptive
Weights
Original base,
RL-adapted α, β
Tests:
RL on original base
3
Improved
+ RL
Improved base,
RL-adapted α, β
Tests:
Kinematics + RL
4
Improved,
No RL
Improved base,
fixed weights
(ablation)
Tests:
Ablation control
2×2 Design: Stages 1 & 2 use the original Braitenberg base · Stages 3 & 4 use the improved base · Stages 2 & 3 add RL weight adaptation · Stage 4 is the key ablation

## Slide 4
EXPERIMENTAL DESIGN
Simulation Environment & Experimental Design
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
Simulation Platform
Arena
800×800 px ≈ 8×8 m (building lobby / open office)
Robot
Radius 10 px (~20 cm) — TurtleBot3 class
Intruder
Radius 15 px (~30 cm) — adult cross-section
Obstacles
Circular, r = 15–30 px (columns, bins, furniture)
Sensors
8 IR proximity sensors (e-puck layout) + PIR target sensor
Speed ratio
Robot 2.0 px/step ÷ Intruder 1.5 px/step = 1.33×
Experimental Protocol
8 Density Levels:
0% Empty corridor
5% Sparse office
10% Furnished office
15% Mixed floor plan
20% Warehouse floor
25% Dense warehouse
30% Industrial space
40% Stress test
4
Layouts
per density
5
Trials
per layout
20
Trials
per density
160
Total trials
per controller
Same seeds & layouts used for all 4 controllers — direct comparison guaranteed

## Slide 5
SYSTEM ARCHITECTURE
Controller Architectures
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
Stage 1 — Pure Braitenberg
Pursuit channel:
Vehicle 2b (excitatory, crossed): target sensor → opposite motor
Avoidance channel:
Vehicle 3a (inhibitory): max proximity per hemisphere → suppress opposite motor
Motor clamp:
v ∈ [0, v_max], negative values clipped to 0
Parameters:
α = 1.0 (pursuit), β = 1.2 (avoidance), fixed throughout
Failure mode:
Stalls above 20% density — avoidance clips both motors to 0
Improved Base (Stages 3 & 4)
Cosine-weighted avoidance:
All 8 sensors contribute: w_i = max(0, cos φ_i) + 0.3 — smoother turns
Forward bias:
b_f = 0.15 px/step added to both motors — prevents stalling when target unseen
Centre-mean motor floor:
If (v_L + v_R)/2 < 0.2, raise both motors — allows asymmetric turns
Stuck recovery:
If displaced < 8 px in 50 steps → 15-step reverse-turn escape
Stage 4 uses fixed α=1.0, β=1.2 · Stage 3 adds RL weight adaptation on top

## Slide 6
SYSTEM ARCHITECTURE
RL Weight Adaptation (Stages 2 & 3)
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
Policy Architecture
Observation o_t (dim = 12)
[p₁…p₈, s_L, s_R, d̂_t, θ̂_t] — 8 proximity + 2 target sensors + normalised distance & bearing
Shared Trunk → Actor + Critic
Linear(12→32) + ReLU
Actor: Linear(32→2) → tanh × 0.5 → (Δα, Δβ)
Critic: Linear(32→1) → V(s_t) (baseline)
α_t = 1.0 + Δα ∈ [0.1, 2.5] β_t = 1.2 + Δβ ∈ [0.1, 2.5]
Training — REINFORCE with Baseline
Algorithm
REINFORCE with baseline (Williams 1992)
All gradients computed analytically in NumPy
Reward
r_t = −0.03·d̂ − 0.15·collided − 0.002 + 15·captured
Training
2,000 episodes · max 2,000 steps/episode
Discount γ = 0.99 · Gradient clip = 1.0
Curriculum
Episodes 1–100: easy densities (0%, 5%, 10%)
Episode 101+: full range (0%–40%)
Learning rates
Actor: 5×10⁻⁴ · Critic: 1×10⁻³ · log σ: 1×10⁻⁴

## Slide 7
RESULTS
Capture Success Rate — All Four Controllers
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
Chart: 
| 0% | 5% | 10% | 15% | 20% | 25% | 30% | 40%
Stage 1 — Pure Braitenberg | 100 | 90 | 60 | 35 | 10 | 0 | 0 | 0
Stage 2 — RL Adaptive Weights | 100 | 80 | 65 | 20 | 5 | 0 | 0 | 0
Stage 3 — Improved + RL | 100 | 100 | 80 | 80 | 55 | 20 | 0 | 0
Stage 4 — Improved, No RL | 100 | 100 | 85 | 90 | 55 | 40 | 0 | 0
Key Findings
Stage 1 fails at 25% — collapses from 60%→0% in two density steps
Stage 2 ≤ Stage 1 at every density — RL adds no value on original base
Stage 3: 80% at 15–20%, 20% at 25% — significantly extends range
Stage 4 equals or beats Stage 3 on capture rate at every density

## Slide 8
RESULTS
Mean Capture Time & Collision Count
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
Mean Capture Time (steps)
Chart: 
| 0% | 5% | 10% | 15% | 20% | 25% | 30% | 40%
Stage 1 | 955 | 1454 | 2679 | 3277 | 3902 | 4000 | 4000 | 4000
Stage 2 | 1072 | 1892 | 2690 | 3638 | 3952 | 4000 | 4000 | 4000
Stage 3 | 869 | 893 | 1853 | 2089 | 3314 | 3509 | 4000 | 4000
Stage 4 | 862 | 867 | 1733 | 1816 | 3044 | 3078 | 4000 | 4000
timeout = 4000
Mean Collision Count (steps)
Chart: 
| 0% | 5% | 10% | 15% | 20% | 25% | 30% | 40%
Stage 1 | 0 | 210 | 138 | 429 | 146 | 50 | 0 | 0
Stage 2 | 0 | 279 | 79 | 125 | 5 | 24 | 0 | 0
Stage 3 | 0 | 51 | 337 | 303 | 508 | 496 | 415 | 199
Stage 4 | 0 | 66 | 346 | 286 | 599 | 583 | 641 | 615
Insight: Stage 3 & 4 capture faster than Stage 1 & 2 up to 25% density. Collision cost is real — Stage 4 peaks at 641 steps at 30% vs Stage 3's 415 steps — but this is the price of not stalling.

## Slide 9
RESULTS
Numerical Summary — All Four Stages
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
Capture Rate (%) · Mean Capture Step · Mean Collision Steps
Density | S1 Rate | S2 Rate | S3 Rate | S4 Rate | S1 Steps | S3 Steps | S4 Steps | S3 Coll. | S4 Coll.
0% | 100% | 100% | 100% | 100% | 955 | 869 | 862 | 0 | 0
5% | 90% | 80% | 100% | 100% | 1454 | 893 | 867 | 51 | 66
10% | 60% | 65% | 80% | 85% | 2679 | 1853 | 1733 | 337 | 346
15% | 35% | 20% | 80% | 90% | 3277 | 2089 | 1816 | 303 | 286
20% | 10% | 5% | 55% | 55% | 3902 | 3314 | 3044 | 508 | 599
25% | 0% | 0% | 20% | 40% | 4000 | 3509 | 3078 | 496 | 583
30% | 0% | 0% | 0% | 0% | 4000 | 4000 | 4000 | 415 | 641
40% | 0% | 0% | 0% | 0% | 4000 | 4000 | 4000 | 199 | 615
Stage 4 capture rate ≥ Stage 3

## Slide 10
DISCUSSION
Failure Mode Analysis — Stage 1 Baseline
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
Stage 1 undergoes a two-phase failure:
Phase 1: THRASHING (5%–15% density)
Robot still mobile — avoidance channel fires repeatedly
Collision count RISES — peaks at 429 steps at 15% density
Oscillatory heading changes as robot bounces between obstacles
Success rate declining but non-zero: 60% at 10%, 35% at 15%
Root cause: max-per-hemisphere aggregation creates hard avoidance jerks
Phase 2: STALLING (>20% density)
Max-per-hemisphere avoidance clips BOTH motors to zero simultaneously
Robot is pinned in place — no forward movement possible
Collision count DROPS (stalled robot hits nothing)
Success rate collapses: 10% at 20%, 0% at 25%+
This structural failure cannot be fixed by adjusting α and β — motivates Stage 3 kinematics
Thrashing (5–15%) → Critical transition (15–20%) → Complete stalling (>20%) — Non-monotonic collision curve is the diagnostic signature

## Slide 11
DISCUSSION
Key Ablation: Stage 3 vs Stage 4
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)
Does the RL policy add value when the base controller is already well-designed?
2 × 2 Design
Original Base
Improved Base
Fixed
Weights
RL
Weights
Stage 1
Original + Fixed
✗ Fails >20%
Stage 2
Original + RL
✗ No improvement
Stage 4
Improved + Fixed
✓ Best capture rate
Stage 3
Improved + RL
✓ Fewer collisions
The Answer
On capture rate: NO
Stage 4 matches or beats Stage 3 at every density. 85% vs 80% at 10%, 90% vs 80% at 15%, 40% vs 20% at 25%. Kinematics alone are sufficient.
On collision count: YES (partially)
Stage 3 incurs fewer collisions above 15% density. The RL collision penalty (λ_c=0.15) works — but only by making the robot more cautious, not better at pursuit.
Practical recommendation
Use Stage 4 if capture rate is the objective. Use Stage 3 only if minimising physical obstacle contact is an independent requirement (e.g., hardware wear).

## Slide 12
CONCLUSIONS
01
Fixed reactive control has a density threshold
Stage 1 (pure Braitenberg) maintains 90–100% capture below 10% obstacle density but collapses to 0% at 25%, driven by a thrashing→stalling transition at 15–20%.
02
RL weight adaptation on the original base adds nothing
Stage 2 matches or underperforms Stage 1 at every density. REINFORCE converges to near-zero weight adjustments — parametric tuning cannot fix a structural kinematic failure.
03
Kinematic improvements are necessary and sufficient
Stage 4 (improved base, fixed weights) extends the operating range to 85–90% at 10–15% and 40% at 25% — matching Stage 3 on capture rate at every density with no training.
04
RL's only measurable contribution is collision reduction
Stage 3's RL policy reduces collision steps at 30–40% density (199 vs 615 for Stage 4) by learning to be overly cautious — useful only if physical wear is an independent concern.
Future: Physical TurtleBot3 validation · Non-circular obstacles · Evasive intruder · Residual policy learning (heading correction)
ME5400A · National University of Singapore · Shridhar Iyer (A0329367R)